Rationale Document for the Logical Data Model

Ground-Warfighter Geospatial Data Model (GGDM) version 2.2

APPENDIX – Component Models

Report Date: December 20, 2013

Contract No W5J9CQ-12-D-0004 Task Order 0008

Unclassified

SAIC, Geo-Spatial Technologies & Information Division

Author:

Annette Janett Filer, SAIC

Contributors:

Robert (Bob) Gaines, SAIC

Dr. Dale D. Miller, SAIC

Dr. Barry Schimpf, Zekiah Technologies, Inc

Nancy Towne, Army Geospatial Center

Prepared for:

U.S. Army Geospatial Center (AGC)

Document Revisions:

- November 17, 2011 GGDM 2.1

- December 20, 2013 GGDM 2.2

Table of Contents

1.	Component Models	1

Topographic Data Store (TDS) Content Specifications	1

AGC Water Resources	3

AGC Engineering Route Study	3

USMC Topographic Production Capability (TPC)	4

FCS Brigade Combat Team Information Model (BCTIM)	4

Army Geospatial Data Model (AGDM) version 1.0 mapped to NFDD	4

NSG Littoral Riverine	5

AGDM/GGDM Change Notices	2

2.	Conclusion	2

Acronyms

This document and associated release materials may make use of several acronyms.

AGC	Army Geospatial Center

AGDM	Army Geospatial Data Model

BCTIM	Brigade Combat Team Information Model

CDMF	Common Data Model Framework

DCS	Data Content Specification

DGIWG	Defense Geospatial Information Working Group

EC	Entity Catalog

EDCS	Environmental Coding Data Standard

EG	Extraction Guidelines

ERS	Engineering Route Studies

Esri	Environmental Systems Research Institute, Inc.

FACC	DGIWG Feature and Attribute Coding Catalog

FCS	Future Combat System (note: this was the name of the program at the time of our initial review)

GGDM	Ground-Warfighter Geospatial Data Model

LDM	Logical Data Model

LRAS	Littoral Riverine Application Schema

LRDS	Littoral Riverine Data Store

MCDB	US Marine Corps Topographic Production Capability Database

NAS		NSG Application Schema

NCGIS	National Center for Geospatial Intelligence Standards

NEC	NSG Entity Catalog

NFDD	NSG Feature Data Dictionary

NGA	National Geospatial-Intelligence Agency

NSG	National System for Geospatial- Intelligence

PDM	Physical Data Model

SBCT	Stryker Brigade Combat Team

SME	Subject Matter Expert

TDS	Topographic Data Store

TGD	Theater Geospatial Database

TGD GPC	Theater Geospatial Database Geospatial Planning Cell

TPC	Topographic Production Capability

UML	Unified Modeling Language

USMC	U.S. Marine Corps

UTP	Urban Tactical Planner

VITD	Vector Interim Terrain Data

WRDB	Water Resources Data Base

# Component Models

In this section, the stakeholder components are described in detail along with their impact to the GGDM, formerly known as the Army Geospatial Data Model (AGDM), and special considerations for each component. Figure 1 shows the stakeholder component models across AGDM/GGDM revisions.

GGDM 2.2 includes all or part of the following stakeholder components:

- National System for Geospatial- Intelligence (NSG) TDS 6.0

- AGDM 2.0.1 which itself is made up of:

  - NSG TDS 3.0, based upon NSG Feature Data Dictionary (NFDD) 3.0 Draft

  - AGC Water Resources Database

  - AGC Engineering Route Study

  - U.S. Marine Corps (USMC) Topographic Production Capability (TPC)

  - Army Geospatial Data Model 1.0 mapped to National System for Geospatial Intelligence (NSG) Feature Data Dictionary (NFDD) 3.0. AGDM 1.0 consisted of data elements from:

    - Theater Geospatial Database (TGD) 3.2

    - Urban Tactical Planner (UTP)

    - Stryker Brigade Combat Team (SBCT)

  - Future Combat Systems (FCS) Brigade Combat Team Information Model (BCTIM)

- Littoral / Riverine. Portions of the draft NSG Littoral Riverine Data Store (LRDS) that were deemed to be of greatest importance to Army and NGA SMEs.

The GGDM process started with the development of each data component within a Common Data Model Framework (CDMF) compliant Logical Data Model (LDM). In some cases the development of the component LDM involved considerable mapping of the source content from the original data dictionary to the current NFDD dictionary. Some of the components were also presented as “partial” components in which the component stakeholder had already performed some mappings or analysis of TDS content and they provided the GGDM team with the known extensions to TDS.

The following paragraphs describe the key components of this GGDM revision:

## Topographic Data Store (TDS) Content Specifications

The NSG TDS and associated Data Content Specification (DCS) 6.0 specifies a subset of the NSG Entity Catalog (NEC) that: “identifies specific content of the NEC that shall be obligatory for geospatial intelligence producers using this specification, and specifies the conditions under which this geospatial intelligence shall be collected by producers for use in net-centric data exchange with other NSG participants.” The TDS focuses only on the topographic content in the NEC. The NEC also contains boundaries, littoral, hydrographic and aeronautical data that are not included in the TDS, even though they may be important for the GGDM.

The TDS version 6.0 does not specify data densities, rather the TDS Extraction Guidelines are specific to data densities and previous revisions of TDS did specify data densities. These data densities remain important to GGDM users and GGDM 2.2 continues to provide information at the data densities (also called configuration levels):

    - Global contains content typically included in topographic datasets/maps at scales of 1:400,000 and smaller;

    - Regional contains content typically included in topographic datasets/maps at scales ranging greater than 1:200,000 up to 1:399,000;

    - Local contains content typically included in topographic datasets/maps at scales ranging from 1:24,000 to 1:200,000; and

    - Specialized-Urban contains content typically included in topographic datasets/maps at scales smaller than 1:24,000.

The TDS DCS is a suite of feature content specifications to support the collection of digital data to populate product-neutral feature databases. It includes an Entity Catalog (EC) describing all of the features, attributes or properties, and domain values found in all data densities and Extraction Guidelines (EG) for each of the four data densities described above. The TDS DCS EC also describes the feature grouping into feature classes, and it specifies the numeric feature identifiers that are required in the physical implementation in Esri physical geodatabases. The TDS DCS EC describes the set of metadata entities to be implemented, but it does not describe how the metadata entities are to be used.

The TDS DCS EC is the primary specification used to develop implementations (physical data models) of the TDS that conform to the National Geospatial-Intelligence Agency (NGA) requirements. The TDS DCS Configuration Level EGs are the primary specifications that are used to guide the collection of data into a conforming TDS implementation.

For the GGDM development, the TDS was required to be a primary component, and it is important that the TDS portion of the GGDM be complete and conforms to the TDS DCS. In particular, the GGDM (the TDS part of it) must be compliant with the TDS DCS EC.

The first step in the GGDM was to create a component LDM for TDS DCS EC 6.0, and apply ancillary additions required to ensure automated generation of accurate Esri physical geodatabases based on the LDM. These additions include the special case “domain” values for Boolean attributes, default values for attributes as indicated by the TDS DCS EC, special attribute codes, and special case attribute alias names. These ancillary additions are required within the LDM in order to automatically generate the Physical Data Model (PDM) using tools.

Within the logical model, relationships are used to associate the feature to group; and feature to configuration level (e.g., global, regional, local, specialized-urban). When the physical model generation tools are run, these relationships are used to allocate features to both feature classes and configuration levels. Relationships between the features and metadata entities as per the TDS DCS EC are included. The metadata relationships are used to generate scripts that either add or remove relationships from the physical models. These relationships can be seen in the Unified Modeling Language (UML) diagrams of the TDS LDM component that were built as well as in the GGDM.

The GGDM PDM tool generation process has been continually refined as it has conformed to modifications made in successive releases of TDS implementations.  As a result, the GGDM PDM representation is expected to closely match the basic content in current Esri implementations of TDS.

## AGC Water Resources

The Water Resources Database (WRDB) is an authoritative data source generated by the AGC and is a required component of the GGDM. AGC personnel evaluated the TDS DCS EC 2.0 for WRDB and Groundwater content and identified concepts that matched TDS DCS EC 2.0 and identified outlying content. This outlying content was documented in a Microsoft® Excel™ spreadsheet and presented to the GGDM team for inclusion in the GGDM as the WRDB required component.

The WRDB spreadsheet and responses to questions about the content were used to form a CDMF-compliant Logical Data Model (LDM) representative of the Water Resources Database and Groundwater data elements that are extensions to the TDS. The WRDB data elements were adjudicated, reusing NFDD concepts wherever possible, refining definitions, refactoring pick-list domain values, and adjusting domain values such as “Other” and “Not Applicable”. While much of WRDB originally was presented using a Defense Geospatial Information Working Group (DGIWG) Feature and Attribute Coding Catalog (FACC)-like data dictionary, explicit mapping tables for WRDB were not developed but were mapped to NFDD on a concept-by-concept basis and resulted in a generated LDM based on NFDD with extensions as needed.

The inclusion of Water Resources Database and Groundwater Extensions resulted in new terms (not found in NFDD or any other standard data modeling dictionary) that were either a) proposed for inclusion within the NFDD, or b) retained by the Army as extensions to the NFDD.  The GGDM 2.2 revision contains updated definitions and labels that are the result of the process of including WRDB extensions into NFDD.

GGDM supported National Center for Geospatial Intelligence Standards (NCGIS) not only in the analysis of WRDB concepts for NFDD, but also in the analysis of WRDB concepts for the NSG Application Schema (NAS). This analysis included a consistency review to ensure water quality attributes were applied to all water related features. As a result of NCGIS NAS changes, the TDS DCS 4.0 included additional WRDB concepts that were not present in the TDS DCS 3.

GGDM 2.2 has refined and expanded WRDB content within the GGDM. Based upon review of WRDB concepts within GGDM 2.1 and the TDS CCB items, several comments and questions were generated and reviewed by WRDB Subject Matter Experts (SMEs). This resulted in the development of specific GGDM change notices that were implemented in the GGDM 2.2. A key change in GGDM 2.2 for WRDB is the addition of several “Areas of Numerous” features representing areas in which numerous water related features or resources are found.

## AGC Engineering Route Study

The Engineering Route Study (ERS) is produced by AGC and is a required component of the GGDM. This component is unique in that the ERS team performed an early evaluation of the TDS and found that all but one required ERS feature was currently present in the TDS. The ERS team provided a list of the required features (no attributes or enumerated domain values) for incorporation into the GGDM CDMF compliant LDM: a) to maintain accurate lineage of features to ERS, ensuring required ERS content will not be inadvertently removed and b) to extend the GGDM with the one feature required by ERS that was not in TDS.

There were no mappings developed for the ERS content and the component LDM is minimal. As the ERS team identifies additional required features or attributes, these will be incorporated into the ERS component LDM such that accurate data requirements for ERS can be tracked against the GGDM.

The GGDM 2.2 included no changes that were a result of ERS activities.

## USMC Topographic Production Capability (TPC)

The USMC TPC (MCDB) content was received as a data base schema (Esri geodatabase). Using the utilities originally developed for reverse engineering of TGD schemas, the schema was extracted, generating a CDMF compliant FACC LDM representing MCDB. Since much of the MCDB is also found in the TGD and most of the mappings for TGD were defined, the unique content in MCDB and not in TGD was the focus. The analysis of MCDB extensions to TGD resulted in additional mapping definitions where the content was understood and mappings were possible. These mappings were included in the AGDM 1.0 mapped to NFDD.

The MCDB mapping resolutions have been documented separately for further review by MCDB SMEs: AGDM_2_MCDB_Rationale.doc.

## FCS Brigade Combat Team Information Model (BCTIM)

The FCS BCTIM was evaluated early in the GGDM development process when there was no NFDD based GGDM to use in a comparison or mappings developed to aid in the analysis. The FCS BCTIM uses an internal data dictionary that is not FACC, but parts of it are similar to the SEDRIS Environmental Coding Data Standard (EDCS), for which there are FACC mappings. The fundamental syntactic, semantic and modeling approach for the BCTIM prohibited evaluation of the BCTIM at the attribute enumerant level, and prohibited analysis with respect to feature geometries. The focus was on the EDCS-like elements within BCTIM that were in common with the AGDM 1.0 and identification of content that fell outside the AGDM 1.0. None of the BCTIM content falling outside of AGDM 1.0 has been included in the GGDM model at this time.

Due to the fact that the AGDM 1.0 was mapped to NFDD and the final GGDM includes lineage statements that indicate where these mappings were used, the BCTIM overlap with the GGDM was identified. The BCTIM lineage documented focuses on those elements of BCTIM found to be in common with AGDM 1.0.

## Army Geospatial Data Model (AGDM) version 1.0 mapped to NFDD

The Army Geospatial Data Model 1.0 was released in February, 2009 and was based on a FACC data dictionary with extensions specific to the model components listed below. AGDM 1.0 was comprised of three primary components:

- Theater Geospatial Database (TGD) 3.2; The Theater Geospatial Database (TGD) is described in 4 levels: Strategic, Operational, Tactical, and Urban

- Urban Tactical Planner (UTP) 0710

- Stryker Brigade Combat Team (SBCT)

AGDM 1.0 was formed by generating a union of the three primary components and then performing adjudication to ensure consistent attribute vectors regardless of geometry, provide for metadata representation, and to abstract geometric representation and common attributes. One goal of AGDM 1.0 was to be inclusive of all of the data content from all of the components. The AGDM 1.0 included hierarchical relationships, abstracted elements, and relationships for feature groupings.

In the development of AGDM 2.0, content that fell outside of TDS was determined and potential extensions to TDS were identified. Almost all of the AGDM 1.0 content was mapped to NFDD. Three different revisions of the TGD-TFDM mapping were developed by NCGIS. Even with this aid there were many cases that new mappings had to be defined to address TGD requirements that were not included in the TGD-TFDM mapping document. Additionally, there were areas that changed over time, mappings had to be re-evaluated, and questionable mappings corrected.

The mapping of AGDM 1.0, evolved into a complex mapping of the data model schema into NFDD 2.0 with extensions, and later updated to NFDD 3 draft with extensions. The complexities include mappings in which feature attribute values from the source may be mapped to multiple destinations including mappings to a feature, or mappings to multiple sets of feature and attribute values. Particularly troublesome were mappings that might violate the consistency of the AGDM (as derived from consistency rules of the TDS). For instance, attribution regarding roads should only appear on roads or other transportation features, not on features that are “near” transportation features: road width should be applied to a road, not a bridge or a tunnel. For more details about the AGDM mapping efforts, please see “GGDM 2.2 RationaleAppendix Concept Mappings.doc”.

The mapping efforts and efforts in making the AGDM look and feel like the TDS resulted in “consistency guidelines” that will be discussed in the next section.

While the AGDM 1.0 included TGD as a component, it did not include the US Marine Corp Topographic Production Capability Database (MCDB). However, since the MCDB content is generally an extension to TGD, the MCDB mappings are included as extensions to the AGDM 1.0 mappings to NFDD.

The AGDM 1.0 stakeholders also apply to the AGDM 2.0:

In particular, the primary stakeholder for AGDM 1.0 was TGD. As such, the primary focus for AGDM 1.0 mappings was on mappings for TGD. The TGD stakeholder has continued to provide key information and feedback in the development of the mappings from TGD to AGDM. Given the importance of the TGD stakeholder and the significant contribution of TGD data requirements within AGDM, documentation has been developed that describes the TGD contributions to AGDM from the TGD perspective. This information is expected to be used to facilitate additional interactions where TGD to AGDM mappings may have had issues, or may need refinement. The TGD Rationale will be documented in: AGDM_2_TGD_Rationale.doc.

The UTP content found within AGDM 1.0 was analyzed by AGC and NSG TDS was found to be inclusive of all required UTP data concepts. For this reason, when a data requirement was found to be present in the AGDM based solely on the source component UTP, it was removed from the AGDM. AGC approved the removal of these concepts. Even so, AGC continues to support Urban Tactical operations and has data sets making use of urban content, primarily from TDS. The AGC Urban Tactical team will continue to take part in AGDM development to ensure the Urban Tactical information is represented accurately and completely.

The SBCT component of AGDM was re-evaluated during this phase and in some cases it was found the SBCT content was represented in TDS or TGD in an alternative fashion and could therefore be removed. While some SBCT concepts were removed from the AGDM, SBCT content was retained if there was clear need and when the definitions were clear. For instance, during meetings with the TGD Geospatial Planning Cell (GPC) SMEs, the need for a Waste Pile or Waste Heap feature was discussed. While this originally came from SBCT, meeting participants stated there was an explicit need for such a concept in the TGD.

## NSG Littoral Riverine

For GGDM 2.2, some of the Littoral / Riverine features were reviewed and excessive attribution was removed. The features identified for Littoral / Riverine as of GGDM 2.1 remain in the current revision of GGDM. The Littoral / Riverine features are:

AerodromeBeacon (Point 00)

AeroNavaid (Point 00)

AquaticVegetation (Area 00)

AquaticVegetation (Point 00)

BottomCharacterRegion (Area 00)

BottomCharacterRegion (Point 00)

CallingInPoint (Point 00)

DepthCurve (Line 00)

DiscolouredWater (Area 00)

DiscolouredWater (Point 00)

DistanceMark (Point 00)

DredgedArea (Area 00)

FishingStakes (Line 00)

FishWeir (Area 00)

FoulGround (Point 00)

Gridiron (Area 00)

Grove (Area 00)

Grove (Point 00)

InsubstantialNavMark (Point 00)

MaricultureSite (Area 00)

MaritimeCautionArea (Area 00)

MaritimeLimit (Line 00)

MaritimeRadarRefLine (Line 00)

MaritimeRoute (Area 00)

MaritimeRoute (Line 00)

MaritimeSignalStation (Point 00)

Marker (Point 00)

MeasuredDistanceLine (Line 00)

SweptArea (Area 00)

TidalStreamObserveStation (Point 00)

TrafficSeparationScheme (Area 00)

TrafficSeparationScheme (Line 00)

TrafficSeparationScheme (Point 00)

WaterbodyDivider (Area 00)

WaterMovementDataLocation (Point 00)

## AGDM/GGDM Change Notices

The AGDM/GGDM change notices coming from Army SMEs, Marine Corp SMEs, AGDM developers, Esri, and NCGIS were researched, reviewed, and documented throughout the development of the GGDM 2.2. These change notices resulted in subtle extension and modification of GGDM content beyond the more direct information listed above. Approved changes were incorporated into the GGDM 2.2 for this release. Generally these changes consisted of changes to ensure consistency with TDS, additional needs for WRDB, and the addition of content for which was declined for the TDS.

# Conclusion

The GGDM is dependent on the component models that are combined and adjudicated to make up the bulk of the information in the GGDM.  Details on the GGDM Extensions to TDS are in “GGDM 2.2 RationaleAppendix Extensions”.

# Footnotes

NSG TDS Content Specification, Version 2.0, 14 August 2009

Analysis of FCS BCTIM and AGDM, version 0.95, 1 April 2010, SAIC

Rationale Document Army Data Model, Spiral 1 May 07, 2008, SAIC

# Text boxes

Figure 1 GGDM Stakeholder Components across Revisions