Rationale Document for the Logical Data Model

Ground-Warfighter Geospatial Data Model (GGDM) version 2.2

APPENDIX – Quality Assurance / Quality Control

Report Date: December 20, 2013

Contract No W5J9CQ-12-D-0004 Task Order 0008

Unclassified

SAIC, Geo-Spatial Technologies & Information Division

Author:

Annette Janett Filer, SAIC

Contributors:

Robert (Bob) Gaines, SAIC

Dr. Dale D. Miller, SAIC

Dr. Barry Schimpf, Zekiah Technologies, Inc

Nancy Towne, U.S. Army Geospatial Center

Prepared for:

U.S. Army Geospatial Center (AGC)

Document Revisions:

- November 17, 2011 GGDM 2.1

- December 20, 2013 GGDM 2.2

Table of Contents

1.	Purpose	1

2.	Scope	1

3.	Quality Assurance/Quality Control Plan Overview	2

4.	Version Control	2

Data Dictionary	3

Component Models	3

Implementations	4

Tools	4

Version Control Conclusion	4

5.	Requirements	4

6.	Tools and Methodologies	5

Esri Database Comparison	5

PIM and PDM Comparisons	2

Common Data Model Framework	2

Tools and Methodologies Conclusion	2

7.	Process	2

Sources To Validate Against	3

Validation Tests Details	4

Test Procedures Using Tools and Methodologies	7

Change Confirmation Process	9

Acronyms

This document and associated release materials may make use of several acronyms.

AGC	Army Geospatial Center

AGDM	Army Geospatial Data Model

CDMF	Common Data Model Framework

DCS	Data Content Specification

EC	Entity Catalog

ERS	Engineering Route Studies

Esri	Environmental Systems Research Institute, Inc.

FACC	DGIWG Feature and Attribute Coding Catalog

GGDM	Ground-Warfighter Geospatial Data Model

GWGE	Ground-Warfighter Geospatial Enterprise

LDM	Logical Data Model

LRDS	Littoral Riverine Data Store

NAS		NSG Application Schema

NEC	NSG Entity Catalog

NFDD	NSG Feature Data Dictionary

NGA	National Geospatial-Intelligence Agency

NSG	National System for Geospatial-Intelligence

PDM	Physical Data Model

PIM	Platform Independent Model

SBCT	Stryker Brigade Combat Team

SME	Subject Matter Expert

TDS	Topographic Data Store

TFDM	Topographic Feature Data Management System

TGD	Theater Geospatial Database

TGD GPC	Theater Geospatial Database Geospatial Planning Cell

USMC	U.S. Marine Corps

UTP	Urban Tactical Planner

WRDB	Water Resources Data Base

# Purpose

The purpose of this document is to establish Quality Assurance/Quality Control (QA/QC) goals, processes and responsibilities required to implement effective quality assurance for both the intermediate components and the final deliverables associated with the GGDM. Generally, these deliverables consist of logical data models (LDMs) and physical data models (PDMs) supporting the Army Geospatial Enterprise (AGE).

# Scope

This plan covers quality assurance activities through the development, release and maintenance phases of the GGDM lifecycle and requires the participation of several organizations that have responsibilities for aspects of the GGDM. These organizations include:

- AGC – Specification of data content for inclusion into GGDM, and select data content including Water Resources Database (WRDB) and Engineering Route Studies (ERS). AGC also has data expertise associated with Urban Tactical Planner (UTP) and Theater Geospatial Database (TGD). AGC participates in GGDM Configuration Control Board (CCB) activities during maintenance, and final quality review and release of the GGDM content.

- National Geospatial-Intelligence Agency (NGA) - NGA and associated entities such as National System for Geospatial-Intelligence (NSG) are responsible for the core NSG Topographic Data Store (TDS) component and related data content including NSG Feature Data Dictionary (NFDD), NSG Application Schema (NAS), NSG Entity Catalog (NEC) and data store drafts for Boundaries, Aeronautical, and Maritime. In addition, NGA’s TDS CCB serves as both an indicator of changes going on with the TDS, and also provides as a mechanism for GGDM extensions to be proposed for inclusion in the TDS.

- Other Government Sources – Several government sources provide SMEs and key input into the GGDM. For example, U.S. Marine Corps (USMC) provides requirements and the comments and participation of Army Geospatial Planning Cells (GPCs) is important input to the GGDM. GGDM success is dependent on quality review and input from these varied government sources.

- SAIC- SAIC is responsible for tools, processes and configuration control, and data model construction and adjudication of the GGDM LDM and is responsible for oversight and management of the GGDM PDMs. In addition, SAIC is also responsible for development of TDS physical databases, as part of the Topographic Feature Data Management System (TFDM).

- Zekiah Technologies, Inc. – Zekiah Technologies develops, manages and supports the GGDM PDMs, Platform Independent Models (PIMs) and tools comparing and validating physical models. Zekiah Technologies also supports GGDM LDM development.

- Esri –  Esri develops TDS physical implementations used as part of the TFDM. Esri also develops tools allowing for database comparison and assists with Subject Matter Experts (SMEs)

The responsibilities of these organizations vary from the definition of versions and schedules to providing data content specifications to data model development and validation. The matrix shown below outlines the responsibilities across these organizations:

|  | Government | Contracting |
| --- | --- | --- |
|  | NGA | Other Govt. | AGC | SAIC | Zekiah | Esri |
| Data Content Provider. Provider of data content specifications and authoritative data dictionaries (NSG TDS, NFDD, NAS, Marine Corp DB, Water Resources DB, Engineering Routes, Stryker Brigade, TGD) | Yes | Yes | Yes |  |  |  |
| Data Content Specification Validation. Responsible for validation of data content specifications and data dictionaries provided to the GGDM team | Yes | Yes | Yes | Yes |  |  |
| Data Content Specification Support. Responsible for providing feedback and support to GGDM team during integration of content into GGDM. | Yes | Yes | Yes |  |  |  |
| Review GGDM for Data Content Specification. Expected to review GGDM results to ensure accurate representation of data content specifications and/or data dictionaries | Yes | Yes | Yes | Yes |  |  |
| GGDM Authority. Authority for GGDM decisions. Lead GGDM control board activities, authorize changes and direct which components shall be adjudicated for inclusion in the GGDM. |  |  | Yes |  |  |  |
| GGDM Schedule and Versioning. Responsible for the schedule identifying versions of incoming content, deadlines, and release dates. |  |  | Yes |  |  |  |
| GGDM Advisory. Advisor for GGDM decisions. Provide input to the GGDM authority in support of the decision making processes. | Yes | Yes | Yes | Yes | Yes | Yes |
| GGDM Data Modeling. Responsible for development of the GGDM logical and physical data models that meet guidelines and directions from GGDM Authority. |  |  |  | Yes | Yes | Yes |
| GGDM Validation. Responsible for the validation of the data model as indicated later in this plan. |  |  | Yes | Yes | Yes | Yes |
| Tools and Methodologies. Responsible for the development of tools that aid in data modeling processes and tools and methodologies that aid in validation and verification of data model content. |  |  | Yes | Yes | Yes | Yes |

# Quality Assurance/Quality Control Plan Overview

Version Control

It is critical that baseline versions be used throughout the process and the quality of the components being used in the process is assured before trying to gauge the quality of the final product. Lessons learned during early GGDM revisions illustrated the difficulties of testing the final product for quality when the underlying components are not yet stable. Within the GGDM processes, configuration management of components, logical models, and physical models are described, ensuring each version is clearly defined and all elements relating to management of the model have clear start and end points.

Requirements

At each level of the process the requirements are clearly identified. Specifically this process identifies the requirements for the LDM, requirements for the PDM requirements, and identifies responsible parties for development and for quality assurance processes.

Tools and Methodologies

The GGDM development employs many semi-automated tools in the development process. The validation process also employs semi-automated tools to ensure the quality of each of the components involved in the development of the model and to ensure the quality of the GGDM. Generally these tools allow for comparison of content and generation of reports showing matching and unmatched content. Several parties responsible for GGDM activities make use of tools in the development of the GGDM and in the validation of the GGDM. Each party provides a slightly different focus and perspective which when combined result in a comprehensive tool set.

Processes

Version control, requirements generation, and tools are combined together into a cohesive and repeatable process by which validation results are generated and evaluated consistently across GGDM revisions. Comparison tests and tools are run and results evaluated for completeness and consistency. Issues involving any model component are documented and assigned to responsible parties for corrective action with expected completion dates.

# Version Control

Versions must be understood, clearly indicated and well managed throughout GGDM development. This includes inputs to the GGDM, the GGDM processes and tools, resulting in generated GGDM content.

Several aspects of the GGDM are subject to version management.

## Data Dictionary

The GGDM is based on a primary data dictionary equivalent to the data dictionary used in the core component, the NSG TDS. The data dictionary changes with each release of the GGDM to match the core component. Currently the GGDM uses NFDD as the baseline data dictionary since the core component of the GGDM is the NSG TDS. One release of the previous model, the Army Geospatial Data Model (AGDM) 1.0 used FACC as the baseline dictionary because the primary component model was TGD. Though the GGDM is based on the NFDD, NFDD is not static and is changed with each revision of the NSG TDS. In some cases, the data dictionary is a draft state when the NSG TDS is merged into a GGDM release.

The Common Data Model Framework (CDMF) manages logical data models as two separable parts: the data dictionary and the data model content. Each is managed and versioned independently and any data model may be based on any data dictionary. This approach allows for greater data reuse and a reduction of data duplication. However, it does mean data dictionary changes affect the data model based on that data dictionary.

Data dictionary changes are important because propagation of a data dictionary change throughout the GGDM can result in a mismatch between the GGDM and the NSG TDS Digital Content Specification (DCS). This is especially important when the mismatch results in the inability of physical implementations to ‘synchronize’. In other words, some DCS content is required to be implemented exactly as specified in the GGDM. Some of the key data dictionary changes and the impact of the changes are:

- Definition changes. The GGDM gets concept definitions from the NFDD. Since the TDS is also based on the NFDD, the definitions should match those found in the TDS Entity Catalog (EC) Digital Content Specification (DCS). However, they do not always match exactly. Since the concept definitions are not critical to synchronization this is not a critical issue and definitions that match the NFDD are acceptable.

- Concept labels and codes. A label or coding change in the dictionary might result in the GGDM being unable to meet synchronization requirement. Early revisions of the GGDM identified several label mismatches at the feature level and all of these have now been corrected in the current NFDD. There have also been issues with attribute labels and codes changing. For this reason the GGDM development processes make use of a secondary attribute label and code that overrides the dictionary settings. Additionally GGDM processes include tests to look for mismatched labels and codes between the GGDM dictionary and the TDS EC DCS.

- New concepts. The GGDM provides for dictionary extensions within the CDMF tool kit. When dictionary extensions in the GGDM become an official part of NFDD the concept is removed from the GGDM extensions area and changes are made to the data model migrate to use the official NFDD concept.

- Concept removal. When concepts are removed from the NFDD and the concept is used within the GGDM, the concept is moved to the GGDM dictionary extensions area. If and when it no longer is required in the GGDM, it is removed.

## Component Models

The GGDM can be thought of as an adjudicated union of several component models where each component model represents data concepts of importance to a particular domain, system, or user. Versioning of component models is important for two reasons:

- The GGDM needs to be built upon stable component models that have received their own validation and verification.

- Experience shows if the component model is in flux and subject to frequent changes, the end products generated can vary and should no longer be used for validation of other products generated from the same component model.

The projection of component model release dates corresponding to the GGDM development schedule is advised to help ensure the GGDM is using the most up-to-date content.

The component models, datasets, and information making up the GGDM include:

- NSG TDS version: 1.3 or 2.0 or 3.0 or 4.0 or 5.0 or 6.0.

- NSG TDS CCB Documents.

- NSG NAS and NEC.

- Draft NSG Data Stores.

- AGC’s Water Resources Database (WRDB), Engineering Route Studies (ERS), and Urban Tactical Planner (UTP)

- AGDM 1.0 mapped to NFDD 2.0. Including:

  - Theater Geospatial Database (TGD) Version 3.2: Strategic, Operational, Tactical, and Urban

  - Urban Tactical Planner (UTP) 07 10

  - Stryker Brigade Combat Team (SBCT)

## Implementations

Implementations include the GGDM itself, both in the logical and physical form, and other implementations to which the GGDM must be interoperable. Specific implementations for which version information is critical include:

- GGDM Logical. The logical data models for the GGDM.

- GGDM Physical. The physical data models for the GGDM including the PIM, and the PDMs in various formats and configurations.

- Esri implementations of TDS, also known as the “TFDM” are checked when possible. Early revisions of GGDM were compared against TDS implementations and there is now more confidence that implementations are consistent. GGDM schema checker tools can be run against Esri TDS implementations to ensure continued consistency.

## Tools

The GGDM process is tools based, and as such the version management of the tools used in the processes and in the validation is important. These tools include:

- CDMF

- PIM and PDM Generation

- Database Comparison

- LDM Consistency Tools

- LDM / DCS comparison

- LDM / LDM Comparison

- LDM / PDM Comparison

## Version Control Conclusion

It should be clear from this extensive list of content making up input and produced in the development of the GGDM version control and version management are critical in the QA/QC process. Validation tests of GGDM must be performed against the correct versions of content and these shall be specified.

# Requirements

It is important to have an understanding of the requirements and explicitly identify the components and/or parties responsible for implementing the requirements. At the highest level, the GGDM requirements are to develop and maintain geospatial information and services capturing the requirements of:

- Geospatial Planning Cells (Theater Geospatial Database (TGD))

- Urban Tactical Planner (UTP)

- Geospatial Elements of Stryker Brigade Combat Team (SBCT)

- National System for Geospatial Intelligence (NSG) Topographic Data Store (TDS)

- Army Geospatial Center (AGC) Water Resources Database (WRDB

- Elements of the Marine Corp Database (MCDB)

- Engineering Route Studies (ERS)

- Boundaries content that was in TDS 3.0 and is being migrated to a new data store

- Littoral/Riverine priority content based on draft Maritime Data Store

Therefore, a key GGDM requirement is the data content found in the logical and physical models shall be traceable and verifiable against the data content specifications listed above.

Requirements specific to the development of LDMs and PDMs include:

- Logical models shall be provided at a level allowing for tools to generate representative physical models.

- Logical models shall describe the data content at the abstract level.

- Logical models shall include enough information to be directly comparable (verifiable) against the source specification.

- Physical model generation tools shall be developed that provide for the translation of logical to physical model.

The TDS DCS is a specification for a physical implementation. Parts of the TDS DCS can be represented within the LDM and other parts need to be left to the PDM. The GGDM logical model must include information specific enough to allow for automated generation of a PDM. To accommodate this requirement, the GGDM Logical model is in fact two transformations of the logical information, one a bit more abstract than the other (the more specific (physical-like) transformation is called the “specification level” and both are described in the document “GGDM 2.2 RationaleAppendix Data Modeling.doc”).

This document details the list of data elements present in the TDS DCS as well as the logical model and physical model. This document also includes a chart listing the parties responsible for validation tests for each data element.

In addition to the version control and requirements going into the process it is also critical that all versions, updates, and changes be received, reviewed and approved by a selected pre-determined cut-off date allowing for sufficient time to integrate, update content and perform validation tests. Validation requires the proper time allocated into the schedule and into the process and a level of rigor difficult but must be enforced to ensure a quality product.

# Tools and Methodologies

Tools are an integral and important part of the GGDM development process and as such, tools are also extremely important in the validation processes. Tools and repeatable processes are also employed during validation by each participant in the validation process.  This section details the tools and methodologies specific to validation.

## Esri Database Comparison

The Data Comparison tool allows for the comparison of an existing database to an updated version of the database. This tool can track the differences between various aspects of the database including the schema, geometry, attributes, and spatial reference. The Esri database comparison tools are used in the verification of the Esri TDS implementation against the GGDM.

The particular items compared for each comparison type are displayed in the table below.

| Comparison type | What is compared |
| --- | --- |
| ALL | Extension class IDs Feature class extents Feature class feature types Feature class shape types Field existence Field length Field type Field var type Subtype default value Table or feature class existence Table row counts XY precision |
| ATTRIBUTES_ONLY | Feature class field values Number of table fields Number of table rows Subtype default values Subtype names |
| GEOMETRY_ONLY | M tolerance Table or feature class existence Z precision Z tolerance |
| SCHEMA_ONLY | Field types Field lengths Field var types Geometry definition M-values Number of table fields Table or feature class existence Table fields Z-values |
| SPATIAL_ REFERENCE_ ONLY | M tolerance XY precision Z precision Z tolerance |

Requirements for this tool are:

- Must report content found in common as well as content that falls outside of either database

- Must report on features (subtypes), attributes, attribute default values, and allowable attribute domain values

- Must work with version 10.0 format content

## PIM and PDM Comparisons

Zekiah Technologies, Inc provides several tools to aid in GGDM verification and validation.  The key tool compares Platform Independent Models and Physical Models in order to compare and contrast the TDS PIM against the GGDM PIM and to compare and contrast one GGDM PIM against another GGDM version. Zekiah Technologies tools can also compare and contrast the GGDM or TDS Physical content against provided Esri physical models. Specific validation capabilities include:

- Identify mismatches between Logical Elements (Feature, Attribute, Enumeration, and Association) and the desired Physical Implementation

- Import and organize the CDMF Logical Model into flattened PIM structures for automated Generation

- Compare Version to Version identifying new, modified, and deleted elements in the GGDM, and/or TDS implementation.

- Create internal statistical analysis accounting for each element from Version to Version, or between CDMF, PIM, and Esri Geodatabase.

## Common Data Model Framework

SAIC makes use of tools throughout the requirements and logical model development processes based on the CDMF. The CDMF provides integrated validation tools to ensure internal database integrity and consistency of the LDM. Specific capabilities CDMF based tools for the GGDM include:

- Extract the DCS spreadsheets into a relational database used for comparison

- Compare the logical model against the DCS

- Compare features, attributes, attribute domain values, data types, cardinality

- Compare different revisions of LDMs

- Compare a geodatabase against the schema defined by the LDM.

The CDMF provides for logical model analysis and correction for all CDMF compliant logical models. These tests and corrective actions include:

- Identify and correct features having no attributes

- Identify and correct attributes not connected to a feature

- Identify and correct issues with primary keys that do not conform to the data elements that make up the key

- Identify and correct null and unused content

- Ensure every attribute has default value

- Ensure every attribute has a domain value list including at least one item

- Ensure all default values are found in the allowable domain value list

- Identify related dictionary issues including:

  - Duplicative classifications, attributes, or enumerants – including checks for duplicative labels, alternative labels, and codes

  - Undefined dictionary terms (content specified in the model with no dictionary entry)

Extended CDMF-based tests specific to GGDM include:

- Verify each feature has a relationship to one group (these are the feature classes)

- Verify each feature has at least one relationship to a configuration level

CDMF Schema checks of geodatabases include:

- Identify missing tables

- Identify missing table subtypes

- Identify incorrect geometry specification

- Identify incorrect subtype identifier numbers

- Identify missing table fields

- Identify incorrect field data type

- Identify missing domain values

- Identify issues with field default values

## Tools and Methodologies Conclusion

Manual methodologies for schema evaluation and comparison of data elements are required at times to ensure GGDM quality. When incorporating schemas into the GGDM, there often is a significant amount of conversion and revisions must be examined to ensure the final representation placed into the GGDM agrees with the final decisions made in the complicated process of schema adjudication. This manual methodology of examination is used for confirmation of many of the change suggestions received throughout the comment period. Multiple change suggestions can affect a single item, and sometimes a single change suggestion can affect a large number of items. It is also possible change suggestions may conflict with later suggestions or processes. Determination that the appropriate and correct change suggestions were incorporated into the GGDM must be confirmed manually.

# Process

Merging the version control, requirements, and tools together into a cohesive repeatable process by which validation results are generated and evaluated answers the following questions:

- What is the process,

- how will it be done,

- who is responsible,

- what is the schedule,

- how will the results be analyzed,

- who will be responsible for identifying changes,

- when will the components be re-examined,

- how will change assurance be performed, and

- who is responsible for each process

Comparison tests and tools are run and the results evaluated for completeness and consistency. Issues involving any model component are documented and assigned to responsible parties for corrective action with expected completion dates.

### Sources To Validate Against

The following are primary sources for which validation tests are performed:

NFDD

The NFDD is referenced within the Digital Content Specifications, the LDM and the PDM. The NFDD is translated from its source format into a CDMF compliant format where it is then used in the LDM and later in the PDM. It is not replicated, it is referenced. The translation reliably retains labels, names, codes from the NFDD. The translation may combine the definition and the description (the description is placed within brackets after the definition).  CDMF based GGDM comparison queries compare the CDMF complaint format LDM against the original NFDD to verify the completeness and correctness of the dictionary. Upon completion of this validation step, there is assurance the dictionary is representative of the NFDD and there is no longer a need to perform validation of definitions or alternative labels. CDMF based GGDM comparison queries compare the CDMF compliant NFDD dictionary against the TDS DCS codes and labels to ensure the dictionary concepts are complaint with the TDS DCS.

TDS DCS

The TDS DCS is the primary specification to which the GGDM must be compliant. This specification is used as a basis for the Esri implementation of the TDS and for the CDMF compliant LDM. It is also used as the primary validation point for all TDS content in the GGDM and the logical and physical representations of the GGDM. SAIC has a tool that reads the Microsoft® Excel™ spreadsheets that make up the TDS DCS and extract all of the content placing it into a relational database where it can later be used for comparisons and queries. The level of confidence in this extraction tool is high given the code is rather simple and has been used successfully to extract multiple previous versions of the TDS DCS, confirming the changed content pulled out by the tool matches the change notices delivered.

Derivations from TDS DCS

(Note: As of GGDM 2.1, all of these codes have been deprecated. However, this section is retained in case other codes are added that must be adjusted in order to be implemented in a PDM.)

There were some derivations from TDS DCS required to implement a physical model. Derived content must be fully defined so such tests may be developed to assess the derived content. The derived content includes:

- PDM Attribute Code: An additional underbar (“_”) is often added in certain PDM formats, to attribute codes, for example: changing LEN to LEN_.

| Attributes having an additional “_” in PDM |
| --- |
| Original Code | PDM Code | Label |
| ASC | ASC_ | Man-made |
| DEC | DEC_ | Deck Count |
| DEP | DEP_ | Depth Below Surface Level |
| FOR | FOR_ | Fortified Building Type |
| LEN | LEN_ | Length or Diameter |
| MIN | MIN_ | Extraction Mine Type |
| WID | WID_ | Width |

- PDM Data Type: Boolean values are implemented physically as enumerated values (as per the DCS). Enumerated values are implemented as integer valued domain values (as per the DCS). These refined data type translations are well defined so tests can be made against the source or destination data types.

  - The DCS specifies Boolean attributes as Enumerated data types. Logically they are Booleans, so the Logical model specifies them as Booleans and they are translated into the Enumerated data type upon PDM generation.

  - The DCS specifies the attribute OTH as an Enumerated data type. However this attribute has no enumerated values and is open to hold any values necessary. The DCS describes how this is done using a string. Therefore, logically and in the physical model, the data type for this particular attribute has been captured as String.

  - The DCS specifies interval attributes as pieces rather than as a single attribute, and this is also how the PDM represents interval attributes. Interval attributes are represented in the Logical model as a single “interval” having the data type of either Real_Interval or Integer_Interval.

  - The DCS specifies attributes having cardinality greater than one by specifically capturing each individual member of the cardinal group. This is also how the physical model provides the attributes. Within the Logical model however, these attributes are captured as a single attribute and the upper bound cardinality is set to a value indicating the maximum allowed number of attributes in the group.

  - The DCS specifies Code List attributes in different manners. Some code list attribute are actually structured text and are implemented as String attributes in the physical model. Other code list attributes are implemented as enumerated domain values in which the selector is text. These code list attributes get their domain value list from a combination of a web site link, and values directly specified in the DCS EC (other and noInformation).

Esri TDS Implementation

It is expected the Esri implementation of TDS (the TFDM) meets the element validation tests this process describes. Therefore an Esri implementation of TDS is directly comparable with the GGDM PDM because the GGDM includes a full subset of the TDS. However, if the GGDM team is made aware of a situation in which the Esri implementation of TDS is not fully compliant with the TDS specification, this information will be taken into account when Esri implementations are compared to the GGDM.

External sources and schemas

There are several external sources from Army and others that provide input to the GGDM. These sources include database schemas, rationale documents, features, attributes, domain values, attribute defaults, change requests and other elements required in a logical model and physical implementation.

In many cases, external sources that form input to the GGDM are derived from schemas and products that have required mapping, adjudication and significant conversion to bring into the GGDM. Manual validation of this content is required to ensure it is correctly represented in the GGDM.

With a discussion of these sources, it is important to consider the level of responsiveness the GGDM development maintains with respect to each of the sources. The process maintains a list of potential sources and the final date for which the source is allowed provide input to the GGDM with respect to each GGDM development cycle.

### Validation Tests Details

Specific validation tests are conducted in which the following elements found within the model (logical or physical) are validated against the source. A template chart is provided indicating the source against which the validation is checked and a column for logical model validation results and physical model validation results where applicable boxes are grey-shaded.  The following chart is used to provide test results. Individual performers may wish to provide detailed test descriptions.

| Elements subject to validation tests | Source of Requirement |
| --- | --- |
|  | NFDD | DCS | Derived | Esri TFDM PDM | Other |
| Feature Container - Esri Feature Class |  |  |  |  |  |
|  | Container/Group Name for features common to TDS must match specification. |  | source |  |  |  |
|  | Container/Group Name for extended features must match NGA specified feature grouping list when applicable. |  |  |  |  | NCGIS |
| Feature - Esri SubType |  |  |  |  |  |
|  | Feature Label must match DCS Feature Physical Label, NFDD Physical Label. DCS adds a geometry indicator to the label |  | source |  |  |  |
|  | Feature Number (TDS features) must match specified SubTypeID |  | source |  |  |  |
|  | Feature Number (extended but in NAS) must match NAS ItemIdentifier_PK when applicable. |  |  |  |  | NCGIS, |
|  |  |  |  |  |  | consistency rules |
|  | Feature Number, extended and not in NAS must be between 1 and 1,000. |  |  |  |  | consistency rules |
|  | Feature Definition must match NFDD Feature Definition/Description | source |  |  |  |  |
|  | Feature Code(TDS features) must match NFDD/DFDD Feature Code as specified in DCS |  | source |  |  |  |
|  | Feature Code(extended features) must match NFDD/DFDD Feature Code + TDS consistency rules |  |  |  |  | NCGIS, |
|  |  |  |  |  |  | consistency rules |
|  | Feature Geometry must match DCS Geometry with some translation accommodated (Area -> Surface, Line -> Curve) |  | source |  |  |  |
| Attribute |  |  |  |  |  |
|  | Attribute Name may match the TDS EC Property Name for attributes common to TDS. Note: These do not have to exactly match. |  | source |  |  |  |
|  | Extended attribute name must be consistent with TDS EC property name. Based on NFDD. | source |  |  |  | NCGIS, |
|  |  |  |  |  |  | consistency rules |
|  | Attribute Code for attributes common to TDS must match DCS Attribute Code. |  | source |  |  |  |
|  | Attribute Code for extended attributes must be based on NFDD, but follow consistency rules established by TDS and NAS. | source |  |  |  | NCGIS, |
|  |  |  |  |  |  | consistency rules |
|  | Attribute Code must match Esri Attribute Code (additional "_" added to some attribute codes). Esri is included as a source because these additional "_" are derived from the Esri TFDM and then applied consistently. |  |  | source | source |  |
|  | Attribute Data Type must match DCS Data Type (with some adjustment for Boolean, Code List, and Other Enumerated values) |  | source |  |  |  |
|  | Attribute Data Type must correlate to PDM Data Type (There is a mapping involved between the DCS specified data type and the data type used in the PDM. For example booleans are implemented as enumerations, and enumerations are implemented as Long Integers). |  |  | source |  |  |
|  | Attribute Length must correlate to DCS Specified Length (Length of "unlimited" shall be set to maximum expected size) |  | source |  |  |  |
|  | Attribute Length must correlate to TDS specified length for attribute common to the TDS (Length of "unlimited" shall be set to maximum physical size) |  | source |  |  |  |
|  | Attribute Definition must match NFDD Definition/Description. Note: TDS DCS Attribute Definitions do not always match NFDD Definition / Description. Furthermore GGDM extends definitions with structure information and http link if needed. | source |  |  |  |  |
|  | Attribute Default Value must correlate to DCS specification for varied data types and in some cases, specific attributes. |  | source |  |  |  |
| Enumeration Value - Coded Value |  |  |  |  |  |
|  | Enumeration Value Number must match DCS Value, NFDD Value | source | source |  |  |  |
|  | Enumeration Value Name must match DCS Value Name, NFDD Value Name | source | source |  |  |  |
|  | Enumeration Value Definition must match NFDD Definition/Description. Definitions are often not specified in the physical model. They also may differ from the NFDD Definition. | source | source |  |  |  |
| Level Container/Group |  |  |  |  |  |
|  | Must correlate to GeoDb Feature Class, DCS Data_Locations. As of TDS v6, some features are not allocated to levels in the TDS DCS. |  | source |  |  | specified in Logical Model |
| Feature Attribute (indication of attribute assignment to features) |  |  |  |  |  |
|  | Must correlate to DCS Feature Attribute List |  | source |  |  |  |
|  | Extended attributes must include rationale where possible. |  | source |  |  |  |
| Feature Attribute Value (assignment of domain values to feature attributes) |  |  |  |  |
|  | Must correlate to DCS Feature Attribute Domain Value List |  | source |  |  |  |
|  | Code List values must be verified against the http reference. |  | source |  |  |  |
| Feature Consistency |  |  |  |  |  |
|  | Features having same code must have the same attribute vector |  | source |  |  | Consistency rules |
|  | Features having same code must have the same attribute domain values |  | source |  |  | Consistency rules |

The QA/QC report for this GGDM 2.2 is contained within the embedded Microsoft® Excel™ document here:

### Test Procedures Using Tools and Methodologies

In the sections above, this document describes tools and methodologies used in the QA/QC processes. Specific usage of tools and methodologies include the following tests and procedures:

| General Validation Process using tools | Tool | Responsible Party |
| --- | --- | --- |
| Comparison between TDS PDM and Esri TFDM |  |  |
|  | Detailed reports indicating differences in features, attributes, domain values, defaults, feature classes and feature subtypes between the TDS PDM and the Esri TFDM. | Esri Comparison Tool | Esri |
| Comparison between GGDM PDM and Esri TFDM |  |  |
|  | Detailed reports indicating differences in features, attributes, domain values, defaults, feature classes and feature subtypes between the TDS PDM and the Esri TFDM. | Esri Comparison Tool | Esri |
|  | Examination of difference reports and confirmation that differences are GGDM Extensions | TBD | SAIC and Zekiah Technologies |
| Comparison between NSG Sample PDM and PDM - this is one method to validate against the DCS |  |  |
|  | Detailed report indicating differences between the NSG representative PDM and the TDS PDM | Zekiah Technologies | Zekiah Technologies |
| Logical Model Component Consistency |  |  |
|  | CDMF tools to validate and correct LDM | CDMF | SAIC |
|  | Expanded CDMF capabilities (GGDM specific) | CDMF | SAIC |
| Logical Model Component Validation against Digital Content Specification |  |  |
|  | Comparison against DCS - report discrepancies | CDMF | SAIC |
| Comparison between LDM and PDM |  |  |
|  | Extract relevant elements from PDM and compare to LDM - report differences | CDMF based geodatabase schema checker | SAIC |
|  | Using lists of PDM elements and LDM elements, compare - report differences | TBD | Zekiah Technologies |
| PDM Validation against Digital Content Specification |  |  |
|  | Extract relevant elements from PDM and compare to DCS - report differences | CDMF based geodatabase schema checker | SAIC |
|  | Extract relevant elements from PDM and compare to DCS - report differences | TBD | Zekiah Technologies |

GGDM content derived from Army or other sources involves mappings, and validation of this GGDM content cannot adequately be described in the tables above. Content originally based on a FACC dictionary does not have matching codes, labels, or aliases or even domain lists upon conversion to the NFDD-based GGDM. The validation tests involving content derived from these sources addresses:

- Validation of the mapping. This includes examination of mapping source and destination content and confirmation the mapping was developed and implemented correctly.

- Accurate lineage of the concepts. When concepts are mapped, it is critical to maintain the lineage of the data content mapped such that destination values can be shown to originate from a specific source.

- Result verification. Resulting content must be examined and traced back through the mapping to the source to ensure accurate mapping was performed and to ensure the intent of the source is not lost.

The GGDM receives validation tests performed by government subject matter experts. These tests include:

- General PDM Validation – Examination and usage tests of the PDM to ensure it operates as expected

- PDM Schema Checks – Examination of selected portions of the PDM against requirements such as DCS to ensure the schema is in compliance.

- LDM and PDM Schema Validation against government provided components – When government sources provide a schema or data set for incorporation into the GGDM, the government performs a verification of the GGDM against those original sources to ensure the results met expectations.

### Change Confirmation Process

The GGDM process includes a review period during which comments may be submitted, and comment adjudication period during which comments are implemented. All received comments are maintained in a directory file structure and database where applicable. Quality assurance with respect to change requests is included in the process and includes:

- Verification all change requests have approved responses

- Confirmation all change requests affecting the GGDM are present in the final revision

Ultimately this process will be enhanced to include change management processes to include comment submission timelines, approval mechanisms, and processes by which change revisions will be implemented and verified.